## Slide 1: R166 – Included in scope
A - Composites Development | Background development for new & improved materials as well as future technology for tensile armour and carcass optimisation / replacement. The background development work will be at the IR&D level and will be coordinated by the project technical lead.
B – Composite Pressure Armour Development | CPA development and qualification. Once the development is complete, the bonded pressure armour will be qualified using a combination of design, analysis of performance, material and subcomponent testing, and finally full scale prototype testing and field trials (Libra to be launch customer – see below). This element of the program will ensure compliance with API & DNV recommended practice as well as all internal Wellstream design and manufacturing guidelines. The CPA technology will also be added to the Wellstream product line through this element of the program (NPI)
C – Module 1_CAPEX | The first module for the compact modular manufacturing line for the composite pressure armour. Key elements: A self-contained & automated tape placement prototype The prototype machine will form the basis for a full manufacturing line design The prototype machine will be able to produce all of the required qualification prototype pipes for the R166 CPA program
D - Libra FEED | Concept Engineering (CE) / FEED study for Libra specific FHC risers design, per Libra Pilot general specifications – The study is to be carried out for both conventional and composite flexibles and will form the basis of the full scale qualification / verification program.
E - Libra – Qualification | Detailed engineering, Testing and Qualification / verification of composite and selected conventional flexible pipe to reach TRL5, then TRL7 via DIP(*) test, to enable delivery of FHC risers within Libra timeline.
F – RPSEA Phase 2b | RPSEA Phase 2b funding awarded to GE. GRC Niskayuna will facilitate a full scale dynamic fatigue test as well as an API mid-scale thermal cycle test on the bonded composite product in 2016. These tests will help accelerate the overall program by validating several technical assumptions. O&G Ncl will supply test pipes using existing prototype manufacturing equipment.