## Slide 1: Development of EPC maturity
Characteristics of different EPC maturity levels vs owners elements and contract types
1. Efficiency
planning & execution
Basic health & safety
Maturity in development chain
Time
2. Effectiveness
design & construct
compliance & QA/QC
Health & Safety
3. Performance
Output & risk transfer
Innovation & optimalisation
environmental & social
4. Life time caretaker
EPC + OM (TCO)
Stakeholder mgt
Private Finance / BOT
No major unforeseen risks
Minimum owners EPCM
Private Finance / BOT
No major unforeseen risks
Design responsibility transfer
Owners EPCM
Fixed scope & price, but quite some risks at Owner
Day-to-day supervision
Owners’ design
Unit based price not fixed
Day-to-day instruction
Owners’ Elements
FIDIC Gold Book
(Design, Build and Operate)
incentives for EPC + O&M
FIDIC Silver Book
(EPC/Turnkey Contract)
incentives for EPC
FIDIC Yellow Book
(Plant & Design Build)
FIDIC Green Book
(Short Form of Contract)
FIDIC Red Book
(Construction contract)
Contract type (FIDIC)

## Slide 2: Typical elements
Characteristics of different EPC maturity levels and what this requires from owners
1. Efficiency
2. Effectiveness
4. Life time caretaker
3. Performance
Workmanship
Work planning
Internal supervisors
Reactive Health & Safety
More work = more revenue
Basic quality standards (ISO9001)
Internal focus
Basic IT
No contract management
No in-house lawyers
No stakeholder management
All elements of level 1
Able to optimize & work out owners’ design
Fully integrated quality policies, control and audits
Health & Safety is actively monitored/reported
Basic certificates similar to ISO45001 and ISO14001
High level of QA/QC
Contract management (subcontractors & client)
Parts of design outsourced
All elements of level 2
Focus on client and performance (improvement)
Design includes Basic Engineering. Familiar with system engineering
Excellent culture of Quality and HSE (visible)
IT: BIM, integrated design packages, 3D modelling
Mgt of design interfaces
Stakeholders mgt EPC phase
In-house legal support
All elements of level 3
Focus on all stakeholders
Design and execution focuses on total costs of ownership & revenue optimization
Managed Services for client
IT: design and operational software is integrated
Senior stakeholder mgt, well connected people
Stakeholder in project
Development experience